## Slide 1: Preprocessors
C Preprocessor is not part of the compiler
It is a separate step in the compilation process.
All preprocessor commands begin with a pound symbol (#)
#define Substitutes a preprocessor macro
#undef Undefines a preprocessor macro

## Slide 2: Preprocessors Examples
#define MAX_ARRAY_LENGTH 20
#undef FILE_SIZE
#define FILE_SIZE 42
#ifndef MESSAGE
#define MESSAGE "You wish!"
#endif

## Slide 3: Program For Macros
#include <stdio.h>
#define message_for(a, b)
printf(#a " and " #b ": Welcome Here…!\n")
int main(void)
{
message_for(Charlie, Jack);
return 0;
}

## Slide 4: Predefined Macros
__DATE__ "MMM DD YYYY" format
__TIME__ "HH:MM:SS" format
__FILE__ This contains the current filename
__LINE__ This contains the current line number as a decimal constant.
__STDC__ Defined as 1 when the compiler complies with the ANSI standard

## Slide 5: Program
#include <stdio.h>
main()
{
printf("File :%s\n", __FILE__ );
printf("Date :%s\n", __DATE__ );
printf("Time :%s\n", __TIME__ );
printf("Line :%d\n", __LINE__ );
printf("ANSI :%d\n", __STDC__ );
}

## Slide 6: C Specifiers
%d format specifier is used for Printing Integer.
%o format specifier is used for Printing Octal.
%x format specifier is used for Printing Hexadecimal.
Any number preceded with Zero (040,050,030) are considered as Octal Numbers.
Any number preceded with [ 0x / 0X ] (0x40,0x50,0x30) are considered as Hexadecimal Numbers.

## Slide 7
%c char single character
%d (%i) int signed integer
%e (%E) float or double exponential format
%f float or double signed decimal
%g (%G) float or double use %f or %e as required
%o int unsigned octal value
%p pointer address stored in pointer
%s array of char sequence of characters
%u int unsigned decimal
%x (%X) int unsigned hex value